## Slide 1
CCMP Action 1 Targets Review (#1,3,4)
Presentation to Estuary Partnership Board of Directors
Keith Marcoe – Physical Scientist
Catherine Corbett – Chief Scientist
September 17, 2026

## Slide 2
CCMP Action 1 Inventory habitat types and attributes in the lower Columbia River and estuary and prioritize those that need protection and conservation; identify habitats and environmentally sensitive lands that should not be altered. Update periodically to reflect emerging science and issues
Objectives
  Identify critical habitat types, and how much of them, to restore and protect
  Measure progress (mapping, etc.) as things change, and adaptively manage
Restoring the biological integrity of the lower Columbia and estuary is the ultimate goal of the Estuary Program

## Slide 3
Preserve Native Habitat Diversity based on the Historic Habitat Mosaic
    - Assumption: historic habitat coverage is proxy for natural habitat diversity
CCMP Steps
Map historical habitats
Map current habitats
Quantify losses
Identify Priority habitats and species
Set quantifiable recovery goals
Measure progress

## Slide 4
Lower Columbia Floodplain Focus
Reach-based analyses (A-H)
Available historic habitat data
EP Study Area
Reporting contemporary habitat change only (1996-Present)
No habitat prioritization or recovery goals
Floodplain Hydrogeomorphic Reaches
EP Study Area

## Slide 5
CCMP 1 Timeline
Map historical habitats (late 1800’s)
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
1800’s Office of Coast Survey topographic sheet
classified in GIS by UW Wetlands Ecosystem Team (Jen Burke)

## Slide 6
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2010)
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
2010 High-resolution landcover/land-use map.
Created for Columbia River Estuary Ecosystem Classification. BPA-funded.
Highly detailed data:
1-meter resolution
Object-based vs. pixel

## Slide 7
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2010)
Quantify losses
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
Cross-tabulation of generalized landcover change scenarios From Marcoe & Pilson, 2017 – Habitat change in the lower Columbia River estuary, 1870-2009

## Slide 8
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2009-10)
Quantify losses
Identify Priority Habitats
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
  Representation of prevalent types, communities
  Representation of rare, vulnerable types, communities
  Ensure many examples of types, communities in each Reach for redundancy
Reach | Priority Habitats |  |  | 
 | 1 | 2 | 3 | 4
A | herbaceous tidal WL | wooded tidal WL |  | 
B | wooded tidal WL | herbaceous tidal WL |  | 
C | wooded tidal WL | herbaceous tidal WL |  | 
D | herbaceous tidal WL | wooded tidal WL | forested | herbaceous
E | herbaceous | forested | shrub-scrub | herbaceous tidal WL
F | forested | herbaceous | herbaceous WL | shrub-scrub
G | forested | herbaceous | herbaceous WL | 
H | wooded WL |  |  | 
  Science Work Group Collaboration
  WL = wetland

## Slide 9
Species
Focal Species and Other Indicator Species Identified through NPCC Sub-basin Plan (2004)
No links to Priority Habitats
Focal Species
Chinook, chum steelhead, coho
Pacific lamprey
Green and white sturgeon
Bald eagle
Columbia White-tailed deer
Ecologically Significant
N. Pikeminnow
Shad
Eluachon
Caspian tern
Osprey
Yellow warbler
Red-eyed vireo
Dusky Canada goose
Sandhill crane
River otter

## Slide 10
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2009-10)
Quantify losses
Identify Priority Habitats
Set Priority Habitat Goals
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
Adapted by A.P. Dobson, 1996
Species-area curves from conservation biology: Macarthur-Wilson (1967), Dobson (1996), Tear et al. (2005), Nature Conservancy.
Most research recommends 30% to preserve common species
50–60% not obtainable in LCRE

## Slide 11
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2009-10)
Quantify losses
Identify Priority Habitats
Set Priority Habitat Goals
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
How much is available ? (‘recoverable habitat’)
Reach A
Reach B
Reach D
Recovery goal for Priority Habitats:
30% by 2030
40% by 2050

## Slide 12
CCMP 1 Timeline
Map historical habitats (late 1800’s)
Map current habitats (2009-10)
Quantify losses
Identify Priority Habitats
Set Priority Habitat Goals
  Create Habitat Restoration GIS Inventory
  Re-map current habitats (2020)
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
2020 High-resolution landcover/land-use map. Created by NV5 Geospatial through NOAA with BIL funding.

## Slide 13
Tracking Habitat Recovery
  Compare landcover maps over time
    Frequency: 10 years
    Better at tracking losses
  Restoration Inventory
    Tracks gains/recovery
    Tracks protected lands
    Limited by reporting accuracy
    Combine results of both to measure progress

## Slide 14
Habitat Recovered and Remaining Goals – 2015 Analysis
Goals met in 2015
Next update in progress
- Add recent restoration activity (2016-2026)
- Add landcover change results (habitat loss)

## Slide 15
Landcover Maps Comparison Results
2010
2020
2010
2020
Real Change
Mapping Inconsistency (water level)

## Slide 16
  Complex classification scheme (hard to separate classes)
  Technology changes
  Inconsistent image collection (date, time, tide cycle, etc.)
  Some can be overcome, but costly
    2010 Map: ~$175k.
    2020 Map: $70k. More errors.
  Alternate solutions
    Simplify classes
    Limit change scenarios (impervious-related, veg. height)
    Use lower resolution products
Landcover Maps Comparison Challenges

## Slide 17
NOAA C-CAP Landcover
Every 5 years
Consistent method
Public data, no cost
Already using for EPA reporting
Spatially limited (30-meter pixel vs. 1-meter object)
Classification scheme different but similar
Still error prone
C-CAP 30-meter, pixel
LCEP 1-meter, object

## Slide 18
Targets 1,4 - Discussion
4: Maintain and update criteria and tools to identify priority species and maps of their priority habitats
  Add language about tracking progress?
  Changes to priority habitats or species?
  Mapping source
    High-resolution worth the cost (~$75-$100k +) ?
  1: Update the map of habitats every ten years
  10-year timeline appropriate?
  Most gains can be measured annually
  Losses require landcover data

## Slide 19
CCMP 1, Target #3
Update and maintain maps that provide information and tools related to vulnerabilities in the estuary due to recurring extreme weather events, accelerated land loss, and sea level rise
Extreme weather: No action
Accelerated land loss:
No action. What is this?

## Slide 20
Sea Level Rise
Evaluated impacts of SLR on lower Columbia wetlands
EPA-funded, 2018 – 2020
0.5, 1.0, 1.5-meter SLR scenarios
Online results
Estuary Partnership Wetlands Impacts Study Online Planning Tool

## Slide 21
Target 4 Adjustment – Revise PH Goals based on SLR analysis
Complicated
  SLR will create and eliminate wetlands
  Uncertainty behind levees
  Available Recoverable Habitat will change
Levee overtopping with 1-meter sea level rise

## Slide 22
Target 3 -Discussion
Extreme Weather Vulnerabilities
  Updated FEMA flood maps
  Proprietary risk maps?
Accelerated Land Loss Vulnerabilities
  Clarify definition or remove
Sea Level Rise
  Rise scenarios still apply
  Results would benefit from
    Better hydraulic modeling & levee assessment
Funding Sources?