## Slide 1
Cold Water Refuges in the lower
Columbia River
Catherine Corbett, Chris Collins, Keith Marcoe,
Paul Kolp, Matthew Schwartz

## Slide 2: Predicted Changes with Climate Change
Climate change impacts:
  Sea level rise –
    Further loss of estuarine and coastal habitat through submersion, conversion and erosion
    More intense storms, increased wave energy, increased erosion
  Changes in upwelling patterns off coast -
    Increased intrusion of hypoxia and acidification into estuaries
    Increased influence with lower summer flows w/precipitation changes
  Warmer temperatures–
    Less habitat for cold water species (salmon, steelhead, trout)
    Species shifts, migration, mortality, increased competition
  Changing precipitation patterns –
    More precipitation falling as rain, lower snow packs in mountains
    Higher winter flows, lower summer flows
    Altered timing and rates of change in flow events
    More and more severe droughts
    Increased pest invasions of forests
    Larger, more severe forest fires
  Vast changes to native habitat conditions and flora/fauna

## Slide 3: Paradigm Shift
Mitigating for Climate Change:
To maintain floodplain wetlands, will need to allow wetlands to migrate inland
  Assess sea level rise, marsh erosion, submersion
  Identify areas - urban, productive agricultural - that will be protected
  Protect more inland, upland areas behind current habitats
  Strategic levee and dike modification
Identify ways to support species ability to adapt
  Provide diversity of habitats to support resiliency of species using them
  Protect, restore base flow, groundwater inputs to tributaries, alluvial fans to provide cold water refugia
  Understand likely changes in habitat structure with increasing temperatures, changing precipitation and inundation, flow patterns
  Understand likely species shifts, migration, mortality, competition
  Adapt management strategies – focus on restoring historic conditions will not be protective of native species in the long term

## Slide 4: Orderly Proactive Transition vs Abrupt Reactive Change
Knowledge and leadership is key

## Slide 5
NWF 2007 - Modeled SLR for Puget Sound to Tillamook Bay
Demonstrates likelihood of significant loss of floodplain habitats
  Inundation, conversion and erosion
  Flooding of urban areas in Astoria, Ilwaco, etc
Good first step BUT need more site specific, detailed information
  Lower Columbia composited with Willapa down to Tillamook Bay (1.4 million acres)
  Covered only up to Cathlamet
  Local planners, officials, funders, restoration practitioners, cannot make significant investment decisions based on these data alone
Mitigating for Climate Change– Sea Level Rise

## Slide 6
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
Current MHHW

## Slide 7
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
1ft Sea Level Rise

## Slide 8
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
2ft Sea Level Rise

## Slide 9
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
3ft Sea Level Rise

## Slide 10
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
4ft Sea Level Rise

## Slide 11
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
5ft Sea Level Rise

## Slide 12
Levels represent inundation at high tide. Areas that are hydrologically connected are shown in shades of blue (darker blue = greater depth).
Low-lying areas, displayed in green, are hydrologically "unconnected" areas that may flood. They are determined solely by how well the elevation data captures the area's hydraulics. A more detailed analysis of these areas is required to determine the susceptibility to flooding.
https://coast.noaa.gov/slr/
6ft Sea Level Rise

## Slide 13
CMOP Stations – operated and maintained by OHSU
Provided by Joe Needoba

## Slide 14
Most natural systems have spatially variable thermal profiles, i.e., not homogenous and not linear (Fullerton et al. 2015)
Mainstem temperatures have increased over the last 70 years
Mainstem temperatures predicted to continue to increase, and extend in duration
Mitigating for Climate Change– Thermal Refuges

## Slide 15
Mainstem thermal regime during juvenile salmon outmigration
UZNG (24˚C)
(Beechie et al. 2012)
Ideal (16˚C)
(Beechie et al. 2012)
Subyearling
Chinook Pass
Bonn. Dam
Regulatory (18˚C)
2015 Mainstem Temps

## Slide 16
Graph and text copied from Keefer et al. 2011.
~50% of steelhead used thermal refugia when temperatures were 19-21°C.
>70% used tributaries when temperatures were > 21°C.
Duration of use extended to weeks during the warmest times.
0
2015 Temps
Mainstem thermal regime during adult returns

## Slide 17
Sockeye salmon
20˚C vs. 16˚C at peak
“These conditions profoundly impacted sockeye passage, travel time and survival. The 2009 to 2014 migration years saw survival of adult sockeye from Bonneville Dam to Lower Granite Dam of 44 percent to 77 percent. In 2015, survival was just 4 percent.” http://www.cbbulletin.com/435505.aspx
USGS video
Lamprey
23˚C at peak
Wild Steelhead
23˚C vs. 21˚C at peak
Summer Chinook salmon
21˚C vs. 18˚C at peak

## Slide 18
Graph and text copied from Keefer et al. 2011
Steelhead returns – run timing by population
Mainstem thermal regime during adult returns

## Slide 19
Assess mouths of tributaries, extent of plumes, temperature differential with mainstem
  Are conditions at mouths sufficient to cue fish to use tributaries?
Received EPA grant for cold water refuges assessment for 15 Gorge tributaries in 2015-2016 (mostly below Bonneville)

## Slide 20
Capacity:
  Temperature: - physiological: <19˚C (Bottom et al. 2011) - protection from predators: <19˚C (Moyle 2002)
    Depth: minimum of ~0.5m for juveniles (Bottom et al. 2005)
    Horizontal extent: uncertain
Organized by attributes presented in Ecological Assessment Criteria for Restoring Anadromous Salmonid Habitat in Pacific Northwest Estuaries (Simenstad and Cordell, 2000)
Opportunity/Access:
  Adjacent to mainstem
  Detection: - Plume must extend into the migratory corridor
  - Temperature differential (2 ˚C differential from mainstem (EPA, ODEQ);
  2-7˚C cued adults above Bonneville) (Keefer et al. 2011)
Question 1: What are the characteristics of thermal refuges?
Our Criteria: >- 2°C temperature difference
- 19°C max. tributary temperature
- >0.5m depth
- max. spatial extent practical

## Slide 21
The likelihood of a plume to form at a tributary confluence is influenced by:
Discharge (tributary and mainstem lower Columbia)
  Columbia River = 100,000 – 150,000 cfs
  Gorge tributaries = 1 – 50 cfs
Water temperature (tributary and mainstem Columbia R.)
  Temperature differential b/t Columbia River and tributaries varies from 2 to 11˚C
Question 2: What factors influence formation of thermal refuges?
QTRIB = 10 cfs
QTRIB = 50 cfs

## Slide 22
The likelihood of a plume to form at a tributary confluence is influenced by:
Discharge (tributary and mainstem Columbia R.)
  Columbia River = 100,000 – 150,000 cfs
  Gorge tributary = 1 – 50 cfs
Water temperature (tributary and mainstem Columbia R.)
  Temp. differential b/t Columbia River and tributary varies from 2 to 11 ˚C
Bathymetric profile (eddy formation)
Atmospheric effects (solar radiation, wind)
Question 2: What factors influence formation of thermal refuges?

## Slide 23: Assessment Results - Stream Temperatures Summer 2015

## Slide 24: Assessment Results - Stream Temperatures Summer 2015

## Slide 25: Assessment Results - Stream Temperatures Summer 2015
Met temperature differential standard
  Temperatures for all tributaries were 2 – 10 degrees Celsius less than the mainstem
Plume formation observed at 5 of 15 tributary complexes
  Bridal Veil, Multnomah, Horsetail, Tanner, Eagle Creeks
  All had discharges > 6 cfs
  Plumes were dynamic, varying with time and water depth
Adult salmonids observed using creeks, with and without plumes
  Tanner, Eagle Creeks
  Lawton Creek confluence, which didn’t have a sign. plume
  Could signify cold water refuge use
Some tributaries lost flow at downstream areas
  Upstream reaches may still provide cold water refuge for salmonids (observed at McCord Creek).
Further study planned in 2016, working with USEPA

## Slide 26: On-Going Cold Water Refuges Work
US EPA under a 2015 NOAA BiOp
Partnering with WA Ecology, OR Department of Environmental Quality, Estuary Partnership
Tasks:
Characterize current spatial and temporal cold water refuges –collecting data at tributary confluences in summer 2016
Characterize current salmon and steelhead use of cold water refuges
Identify potential locations to restore cold water refuges
Assess whether current cold water refuges is sufficient to meet Oregon’s narrative temperature criteria
Characterize additional cold water refuges needed
Identify and prioritize actions to protect, restore or enhance cold water refuges

## Slide 27
Science to Policy Summit
Climate Change: How vulnerable is the
lower Columbia River?
Questions?